SIDD-CA Specification

TYPICAL SPECIFICATIONS

Model: SIDD-CA

Description: Fan shall be of the "Square in-line" type with a square inlet and outlet. Fan shall be designed for floor mount or hung installations in-line with ducting, and have a direct driven centrifugal wheel. Fan shall be a corrosion resistant steel, direct driven, square inline blower.

Application: Square In-Line Duct Blowers are suitable for various applications. Commonly mounted indoors with both inlet and outlet ducts to supply or exhaust air. Square In-Line Duct Blowers are engineered to discharge air, fumes and other contaminants horizontally in a duct.

Certifications: Square In-line Duct Blower(s) shall be licensed to bear the AMCA Certified Ratings Seal for Air and Sound Performance and be ETL Listed to UL705 Standards.

Construction: Square In-line Duct Blower(s) shall be constructed of galvanized steel. A removable cover shall provide blower motor access, and drive access shall be provided on both sides through removable panels. Blowers shall be direct driven; centrifugal backward inclined.

Housing

The blower shell shall be constructed of heavy-gauge galvanized steel. Side panels shall be removable for service access.

Wheel

Backward inclined non-overloading, all-aluminum wheel. Balanced in accordance with AMCA standard 204-96, Balance Quality and Vibration Levels for Fans.

Motor & Motor Compartment

Motor shall have permanently lubricated ball bearings and be of voltage, phase, and enclosure as specified. A motor cover shall be supplied as standard.

Product: Fan shall be model SIDD-CA as manufactured by CaptiveAire Systems.